## Slide 1: Engineering Mechanics Course code: 116U06C104
Module 1: System of Forces
1.1: System of coplanar forces
Faculty: Dr. Manish Deo

## Slide 2: Learning Outcome
Students will be able to calculate the resultant of
Coplanar concurrent force system
Students will be able to calculate the moment of
force about a point.
Students will be able to apply Varignon’s
theorem

## Slide 3: Mechanics Definition and Classification
Definition
The branch of physical science which is concerned with study of resultant, effect of action of force on bodies, both in the state of rest and in motion.[14]
Classification
    Mechanics of rigid bodies
    Mechanics of deformable bodies
    Mechanics of fluids (Fluid Mechanics)

## Slide 4: Rigid Body Mechanics
In rigid body mechanics, bodies are assumed to be perfectly rigid, i.e. there is no deformation of bodies under the action of loads to which they are subjected.
Although Engineering machines and structures do deform under the action of loads, their deformation is so little, that it does not affect the conditions of equilibrium or equations of motion which are applied in their study.

## Slide 5: Mechanics of Rigid Bodies (Engineering Mechanics) Classification

## Slide 6: Engineering Mechanics definitions

## Slide 7: Fundamental Concepts of Mechanics
Length:
Position of a point in space w.r.t. origin.
Size of a system
Time:
For bodies in motion

## Slide 8: Fundamental Concepts of Mechanics
Mass:
    Quantity of matter contained in a body.
    Remains unchanged irrespective of the position occupied by
    the body.
Force:
    Action of one body on the another body.
    The action could be ‘push’ or ‘pull’.
    The force is exerted when there is actual contact between the two bodies or without contact like: gravitational force or magnetic force etc.
    Force requires: Magnitude, direction, point of application

## Slide 9: Pull – Push Force
Fig. 1 Pull – Push forces[1]
PULL
PUSH

## Slide 10: Classification of Force System
Fig. 2 Classification of Force system

## Slide 11
Fig. 2 Classification of Force system

## Slide 12: Force
Fig. 3 Force system[2]

## Slide 13: Particle and rigid body
Particle: It is a matter with considerable mass but negligible dimension.
  Eg. Train, Artificial satellite
Rigid body: It is a matter with considerable mass as well as dimension.
  Eg. Columns and beams of structure

## Slide 14: Point load
The load of a body at contact surface acting over a certain area, is assumed as acting at a point, for simplicity and calculation.
Fig. 4 A block kept on the floor[2]
Fig. 5 A ball in contact with ground[2]

## Slide 15: Principle of Transmissibility of force
According to the principle of transmissibility of force, the uniform motion of rigid body or the condition of equilibrium will remain unchanged if the point of application of a force acting on a rigid body is transmitted to act at any other point along its line of action.
Fig. 6 Push force conversion to pull force[2]

## Slide 16: Law of parallelogram of force
According to this law,
if the two forces acting simultaneously on a body at a point are represented in magnitude and direction by two adjacent sides of a parallelogram, then their resultant is represented in magnitude and direction by the diagonal of parallelogram which passes through the point of intersection of the two sides representing the forces.
Fig. 7 Law of parallelogram of force[2]

## Slide 17: Law of parallelogram of force
Fig. 7 Law of parallelogram of force[2]

## Slide 18: Composition of Forces
Forces may be combined (added) to obtain a single force which produces the same effect as the original system of forces.
This single force is known as resultant force.
The process of finding the resultant of forces is called composition of forces.
Force is a vector quantity. The method of addition of forces (vectors) is based on the parallelogram law.
Fig. 7 Law of parallelogram of force[2]

## Slide 19: Composition of Forces
Based on the parallelogram law.
Fig. 8 Law of parallelogram of force[2]

## Slide 20: Composition of Forces
Based on the parallelogram law.
Fig. 9 Triangle law of forces (Corollary of parallelogram of force)[2]

## Slide 21
Fig. 2 Classification of Force system

## Slide 22: Resolution of Forces: Into oblique components of forces
The process of breaking the force into a number of components which are equivalent to the given forces is called resolution of force.
The law of parallelogram shows how to combine the forces into a resultant force whereas resolution of force is an inverse operation in which a given force is replaced by two components which are equivalent to the given force.
Fig. 11 Resolution of force into oblique components of force [2]

## Slide 23: Resolution of Forces: Into Rectangular coordinates
The process of breaking the force into mutually perpendicular components, which are equivalent to the given force, is called rectangular components of force.
Fig. 12 Resolution of force into perpendicular components of force [2]

## Slide 24: Resolution of Forces: in to Rectangular coordinates

## Slide 25: Resolution of Forces: Into Rectangular coordinates
The process of breaking the force into mutually perpendicular components, which are equivalent to the given force, is called rectangular components of force.
Fig. 12 Resolution of force into perpendicular components of force [2]
Sign Convention:

## Slide 26: Numerical on Composition of Forces
Q. 1
Fig.10 Numerical[2]

## Slide 27: Resolution of Forces (Numericals)
Fig. 13 Moment of force [2]
Q. 2

## Slide 28: Resolution of Forces(Numericals)
Fig. 14 Moment of force [2]
Q. 3

## Slide 29: Resolution of Forces (Numericals)
Fig. 15 Moment of force [2]
Q. 4
(a)

## Slide 30: Resolution of Forces (Numericals)
Q. 5 Find the Fouth force(F4) R=800 N is the resultent of 4 concurrent forces.

## Slide 31: Resolution of Forces (Numericals)
Q. 6

## Slide 32: Moment of Force
The rotational effect of forces is
called as moment of force.
Rotational effect has to be
with respect to a point.
The concerned point is known as
the moment centre
This perpendicular distance is known as moment of arm
Fig. 16 Moments of force [2]

## Slide 33: Moment of Force
Fig. 16 Moments of force [2]
Rotational effect or moment of force : Product of force and the perpendicular distance from moment centre to the force
Tendency to rotate clockwise or anti-clockwise

## Slide 34
Q. 7 Find the resultant moment of all the forces about A

## Slide 35: Moment of Force (Numericals)
Fig. 17,18 Moment of force [3]
Q. 8
Q. 9
Fig. 17
Fig. 18
Ans: 275N

## Slide 36: Couple
Fig. 19,20 Couple [3]
Two parallel forces of equal magnitude and opposite senses form a couple.
Effect: Rotate a body on which it acts.
Moment of Couple:
M = F X d
Sign convention:
    Anticlockwise : + Ve
    Clockwise: - Ve
Fig. 19 Fig. 20

## Slide 37: Properties Couple

## Slide 38: Couple (Numerical)
Fig. 21
Q. 10
Fig. 21,22 Couple [2]
Q. 11
Fig. 22
Calculate the couple

## Slide 39: Resolution of Concurrent Forces (Numerical)
Q. 13

## Slide 40: Resolution of Concurrent Forces (Numerical)
Q. 12
Fig. 24 Resultant of concurrent Forces [2]
A car is pulled by means of two ropes as shown in Fig. 24. The tension in one rope is P = 2.6 kN. If the resultant of two forces applied at O is directed along the x-axis of the car. Find the tension in the other rope and magnitude of the resultant. (Q = 2.934 kN, R = 4.8 kN ( )

## Slide 41: Resultant of Concurrent Forces Using Method of Resolution
Following steps to adopted if more than two forces are acting at a point:
Step I: Resolve the inclined forces if any along the horizontal X –direction and the vertical Y – direction
Step II: a) Calculate the sum of resolved horizontal forces to get, ΣFx (following sign convention: +Ve
b) Calculate the sum of resolved horizontal forces to get, ΣFy (following sign convention: +Ve
c) Resultant:

## Slide 42: Resultant of Concurrent Forces Using Method of Resolution
Following steps to adopted if more than two forces are acting at a point:
Step III: To determine the direction of resultant w.r.t. X – axis θ, following steps to be followed:
Take +ve values of and in the following relation to obtain θ:
(Angle will be less than 900).

## Slide 43: Resultant of Concurrent Forces Using Method of Resolution
Following steps to adopted if more than two forces are acting at a point:
Step IV: Based on the of decide the quadrant of the resultant.
Step V: Draw the diagram showing the direction of the resultant.
Condition | Position of Resultant
+ Ve and + Ve | 1st Quadrant
- Ve and + Ve | 2nd Quadrant
- Ve and - Ve | 3rd Quadrant
+ Ve and - Ve | 4th Quadrant
Condition | Position of Resultant
 | 1st Quadrant
 | 2nd Quadrant
 | 3rd Quadrant
 | 4th Quadrant

## Slide 44: Resolution of Concurrent Forces (Numerical)
Q. 14
Fig. 26 Resultant of concurrent Forces [2]

## Slide 45: Resolution of Concurrent Forces (Numerical)
Fig. 26
Q.15. Forces 7 kN, 10 kN, 10 kN and 3 kN, respectively act at one of the angular point of regular pentagon toward the other four points taken in order. Find their resultant completely.
(R = 25.10 kN, θ = 45.690)
Fig. 27 Resultant of concurrent Forces [2]

## Slide 46: Resolution of Concurrent Forces (Numerical)
Q. 16

## Slide 47: Couple (Numerical)
Q. 17
Fig. 23 Couple [3]

## Slide 48: Numerical on Coplanar Parallel Forces
Fig. 29 Coplanar parallel Forces [2]
Q. 18 Determine the resultant of Force system shown in Fig. 29
Fig. 29

## Slide 49
Q. 19

## Slide 50: Numerical on Coplanar Parallel Forces
Q. 20 Fig. 30 shows four parallel forces acting on a beam ABCD.
Determine the resultant of the system and its location from A.
Replace the system by a single force and a couple acting at point B.
Replace the system by a single force and couple acting at point D>
Fig. 30

## Slide 51
Q. 21 Fig. shows a parallel system of four forces and two couples.
Replace the system by a single force and obtain its location from A
Replace the system by a force couple system at point A.
Replace it by a force couple system at point D

## Slide 52: Varignon’s Theorem
Fig. 28 Varignon’s Theorem [2],[3]
It states that
Moment of the resultant of all the forces in plane about any point is equal to the algebraic sum of moments of all the forces about the same point.

## Slide 53: Varignon’s Theorem
Fig. 28 Varignon’s Theorem [2],[3]

## Slide 54
Q. 22 Determine the resultant of the parallel Force system and locate it w.r.t. to O, if its radius is 1 m.

## Slide 55: Numerical on Coplanar Non Concurrent – Non Parallel Forces
Fig. 34
Q. 23 A triangular plate ABC is subjected to four coplanar forces as shown in Fig. 34. Determine the resultant completely and locate its position w.r.t. point A.
Fig. 34 Coplanar Non Concurrent Non - Parallel Forces[2]

## Slide 58
Q. 24 Determine the resultant of the forces system shown in fig and
position where the resultant cuts the X axis

## Slide 60: Numerical on Coplanar Non Concurrent – Non Parallel Forces
Fig. 35 Coplanar Non Concurrent Non - Parallel Forces[3]
Fig. 35
Q. 25 A system of forces of acting on a bell crank lever is shown in Fig.
Determine the magnitude, direction and the point of application of the resultant w.r.t ‘O’. Also determine the location of the resultant on the horizontal arm of the lever. (R = 2671.2 N at theta = 80.3 at perpendicular distance d = 139.17 mm to left of O. X = 14.12 cm left of O

## Slide 62
Fig. 37 Coplanar Non Concurrent Non - Parallel Forces[3]
Q. 26 Determine the resultant of the given coplanar system of forces and a couple.
Also locate the resultant on the X axis w.r.t the origin.
Reduce the system to a force couple system at O.
This is a general force system, since the lines of action of all forces don‟t meet
at a single point.
Calculations of angles:

## Slide 63
Magnitude of the resultant
Direction of the resultant

## Slide 65
Fig. 36
Q. 27 Three forces 1 kN, 3 KN and 2.5 kN act on a vertical pole 6 m high.
Determine:
The magnitude, direction and position of resultant w.r.t. A.
The position where the pole cuts the pole from the base.
Reduce it to a force couple system at A.

## Slide 66: Reference
https://commons.wikimedia.org/wiki/File:Thrust-force-simple.svg
‘Engineering Mechanics’, N.H. Dubey, Tata McGraw Hill Publication, 2017, page no: 1.1 to 1.25
‘Engineering Mechanics’, M.D. Dayal, page no: 14,24